Bootloader communication protocol
Protocol version: 1

Default connection settings (via UART)
- baudrate: 57600;
- 8 data bits;
- 1 stop bit;
- no parity control.

Bootloader enter (default)
To enter bootloader pull specified in HAL/Defines.inc pin (ListenPind) to ground and then reset MCU. If bootloader started, then LedPin, specified in the same file, will become high.

Commands

Device identification
Send one byte to device:
'I' (ASCII 0x49)	(1 byte)

Bootloader will answer:
'FBL' – bootloader signature	(3 byte)

VER – protocol version, currently = 0x01	(1 byte)

VID2 VID1 VID0 – vendor identitier (most significant byte first)	(3 bytes)

MID2 MID1 MID0 – model identifier (most significant byte first).	(3 bytes)

SN3 SN2 SN1 SN0 – device serial number (most signiticant byte first).	(4 bytes)

Totally response consist of 14 bytes.
Issue this command first to identify device.

FLASH page write:
Send two bytes to device:
'W' (ASCII 0x57)	(1 byte)

PGADDR – page address (aka page number).	(1 byte)

Device checks page addres and returns one byte:
0x00 — address is correct, device is ready to accept data,
or
0x01 — address is incorrect (e.g. attempt to write into read-only bootloader pages).

If address is correct, you need to send data to write. Send:
DATA — data to write, byte at the lower address first.	(page size bytes)

When all bytes is received, page is being erased and rewritten. When rewrite is completed device returns:
0x00	(1 byte)

After getting this 0x00 byte you are free to issue next command.

FLASH page read
Send two bytes to device:
'R' (ASCII 0x052)	(1 byte)

PGADDR – page address	(1 byte)

Device reads page (any page can be read, including bootloader) and returns:
0x00 – page read successfully
or
0x01 – error happened.

If page read successfully, then after 0x00 immediately follows
DATA – page data, byte at lower address first	(page size bytes)

EEPROM write:
Send to device
'w' (ASCII 0x77)	(1 byte)
BYTE – first byte to write (EEPROM address 0x00)	(1 байт)

Device writes byte and returns:
'n' – in this case send next data byte	(1 byte)
ИЛИ
'f' – in this case operation is completed	(1 byte)

EEPROM read:
Send to device:
'r' (ASCII 0x072)	(1 byte)

Device reads EEPROM and returns:
DATA – EEPROM content (byte for 0x00 address first)	(EEPROM size bytes).

Firmware exit:
Send to device:
'Q' (ASCII 0x51)	(1 byte)

Device will answer:
'B' (ASCII 0x42)	(1 byte)
and reboot into the main firmware.